## Slide 1
Analytic Computing
Fachpraktikum
Maritime Anomaly Detection
08.02.2023
Qiuming Li
Zhenhao Xu

## Slide 2
Motivation
MV Golden Ray capsized on 08.09.2019 within the Port of Brunswick's harbor
The ferry MV Sewol sank on the morning of April 16, 2014, an route from Incheon towards Jeju in South Korea, 306 died in the disaster, including around 250 students.
The automatic detection of abnormal behaviour of vessels in ports and sensitive waters and the implementation of early warnings are of great importance in ensuring water traffic safety.

## Slide 3
AIS: Automatic Identification System
MMSI | BaseDateTime | LAT | LON | SOG | COG
367369550 | 2019-09-08T00:00:06 | 31.14314 | -81.49662 | 12.3 | 122.8
AIS is an automated, autonomous tracking system that tracks the location of vessels anywhere they are in the world.
MMSI: Maritime Mobile Service Identity, LAT/LON: latitude/longitude
SOG: Speed over Ground, COG: Course over Ground

## Slide 4
A segment contains the information about a ship's journey over a 10-minute period.
One AIS signal point of one ship per minute can be acquired, but sometimes some signal points may be lost. So in a ten-minute period, we can get up to 10 signal points of a ship.
The colour here is only to distinguish the segments
What is our goal？
Our goal is to detect if this segment is anomalous!!
What is segment？

## Slide 5
Method: Supervised learning
Treat all real data as normal
Set up abnormal scenarios and simulate abnormal data
Treat all simulated data as anomalous
We use supervised learning to train the model, so we need to set labels for the dataset to distinguish between abnormal and normal data.

## Slide 6
Feature Selection
SOG: Speed over Ground
COG: Course over Ground
Distance: Distance between coordinates of two subsequent measurements.
SOG
COG
Data
point1
Data
point2
Difference longitude
Difference latitude
Distance
So we select 3 Features for each time points, and each segment have max. 10 time points. Each segment is represented as an array of shape 10 x 3.

## Slide 7
Data Generation
Firstly generate points and then make segments

## Slide 8
Data preprocessing
Real Data
Real Regional Data
N normal segments of shape 10 x 3
Abnormal Data Generation
M abnormal segments of shape 10 x 3
Combine as (N+M) x 10 x 3
Label each segment as normal/abnormal. Save as (N+M) x 2.
Model
Select Region
Segmentation

## Slide 9
Model: 1D Convolutional Neural Network
Why 1D-CNN Model?
“A 1D-CNN Based Deep Learning Technique for Sleep Apnea Detection in IoT Sensors, (ISCAS) 2021”
“Classification of ECG Signals Based on 1D Convolution Neural Network, (Healthcom) 2017”
The 1D-CNN model is widely used for anomaly detection of time-series data like ECG signals, and AIS signals are also time-series data, so we think it is very appropriate to use the 1D-CNN model
Compared to models such as RNN-based LSTMs, 1D CNNs have the advantage of being fast to train and can be computed in parallel.

## Slide 10
CNN-Model structure
Convolution 1st layer
Convolution 2nd layer
Max Pooling
Convolution 3rd layer
Max Pooling
Dense 1st layer
Flatten
Dense 2nd layer
Dense 3rd layer
Dense final layer
Input, shape: 10x3
Output, shape: 1x2

## Slide 11
Train/Test Dataset
Train Dataset:
->317 segments real normal data in 2019_01_01 in selected area
->132 segments from random generation abnormal data in selected area
Test Dataset:
->211 segments from real normal data in 2019_06_01 in selected area
->112 segments from random generation abnormal data in selected area
Dataset for real accident test:
->537 segments from real normal and abnormal data in 2019_09_08 in the area the accident happens
->443 segments from real normal and abnormal data in 2019_09_07 in the area the accident happens

## Slide 12
Evaluation
Confusion Matrix |  | Predicted results | 
 |  | Negative | Positive
Ground Truth | Negative | True Negative(TN) | False Positive(FP)
 | Positive | False Negative(FN) | True Positive(TP)
For example:
For example:
Precision reflects the ability of the model to discriminate between negative samples.
Recall reflects the ability of the model to discriminate between positive samples.
F1 score is a combination of both

## Slide 13: CNN-Model1
Results analysis and optimization of models and datasets
use 2 features: SOG COG
CNN-Model2
use 3 features: Distance SOG COG
Dataset_1
If there are missing signals in each segment, supplement missing signals with 0.
But in generation data there is no missing signal
Result_1(D1-M1) and Result_2 (D1-M2)
 | Dataset_1
CNN-Model_1 | D1-M1
CNN-Model_2 | D1-M2
We did 7 tests with different models and datasets pairings

## Slide 14
Statistics View of Result_1 (D1-M1) and Result_2 (D1-M2)
 | Dataset_1 | Dataset_2 | Dataset_3
CNN-Model_1 | D1-M1 | Result_3 | Result_5
CNN-Model_2 | D1-M2 | Result_4 | Result_6
Chart: 
| D1-M1 | D1-M2 | D2-M1 | D2-M2 | D3-M1 | D3-M2
Abnormal precision | 0.915 | 0.958 | 0.739 | 0.508 | 0.812 | 0.947
Abnormal recall | 0.827 | 0.885 | 0.298 | 0.579 | 0.616 | 0.804
Segments in real data:
Segments in generation data:
This is the differences we don‘t want the model to take into account.
One Segment
Signal Point
Missing Signal Point
One Segment
Signal Point

## Slide 15
Dataset_2
If there are less than 3 signals in one segment, drop it. otherwise supplement missing signals with 0
And in generation dataset there is random missing signals and supplement with 0
Dataset_1
If there are missing signals in each segment, supplement missing signals with 0.
But in generation data there is no missing signals
 | Dataset_1 | Dataset_2
CNN-Model_1 | D1-M1 | D2-M1
CNN-Model_2 | D1-M2 | D2-M2
Result_3 (D2-M1) and Result_4 (D2-M2)
One Segment in generation data
Signal Point
Randomly add missing signal points

## Slide 16
 | Dataset_1 | Dataset_2 | Dataset_3
CNN-Model_1 | D1-M1 | D2-M1 | Result_5
CNN-Model_2 | D1-M2 | D2-M2 | Result_6
Statistics View of Result_3 (D2-M1) and Result_4 (D2-M2)
Chart: 
| D1-M1 | D1-M2 | D2-M1 | D2-M2 | D3-M1 | D3-M2
Abnormal precision | 0.915 | 0.958 | 0.739 | 0.508 | 0.812 | 0.947
Abnormal recall | 0.827 | 0.885 | 0.298 | 0.579 | 0.616 | 0.804
The model cannot simply distinguish between real and generated data by the number of missing signals in the segment
But there is too little Information in each segment.

## Slide 17
Dataset_2
If there are less than 3 signals in one segment, drop it. otherwise supplement missing signals with 0
And in generation dataset there is random missing signals and supplement with 0
Dataset_1
If there are missing signals in each segment, supplement missing signals with 0.
But in generation data there is no missing signals
 | Dataset_1 | Dataset_2 | Dataset_3
CNN-Model_1 | D1-M1 | D2-M1 | D3-M1
CNN-Model_2 | D1-M2 | D2-M2 | D3-M2
Result_5 (D3-M1) and Result_6 (D3-M2)
Dataset_3
If there are less than 5 signals in one segment, drop it. otherwise supplement missing signals with 0
And in generation dataset there is random missing signals and supplement with 0

## Slide 18
 | Dataset_1 | Dataset_2 | Dataset_3
CNN-Model_1 | D1-M1 | D2-M1 | D3-M1
CNN-Model_2 | D1-M2 | D2-M2 | D3-M2
Statistics View of Result_5 (D3-M1) and Result_6 (D3-M2)
Chart: 
| D1-M1 | D1-M2 | D2-M1 | D2-M2 | D3-M1 | D3-M2
Abnormal precision | 0.915 | 0.958 | 0.739 | 0.508 | 0.812 | 0.947
Abnormal recall | 0.827 | 0.885 | 0.298 | 0.579 | 0.616 | 0.804

## Slide 19
Statistics View of Result_6 (D3-M2) and Result_7 (D3-SVM)
 | Dataset_3
CNN-Model_1 | D3-M1
CNN-Model_2 | D3-M2
SVM-Model | D3-SVM
Chart: CNN VS SVM
| D3-M2 | D3-SVM
Abnormal precision | 0.947 | 0.85
Abnormal recall | 0.804 | 0.39
Performance of CNN-Model is better than SVM-Model

## Slide 20
Map View of Results
M1-D3(use 2 features)
M2-D3(use 3 features)
 | Predicted Negative | Predicted Positive
Actual Negative | Red (TN) | Blue (FP)
Actual Positive | Yellow (FN) | Green (TP)

## Slide 21
Real accident test
Real accident description：The MV Golden Ray was a 200-metre long (660 ft) roll-on/roll-off cargo ship，On 8 September 2019 at approximately 0137 EDT, the Golden Ray capsized within the Port of Brunswick's harbor, shortly after unberthing and proceeding towards the Port of Baltimore.
The colour here is only to distinguish the segments
Wikipedia's reliable information on the location of the incident:
AIS data of the ship at the time of the incident that we found in the dataset:

## Slide 22
Performance of the Model Predict for real accident
Results from the Day of accident: 08.09.2019
 | Abnormal | Normal
Predict | Yellow | Green
Location of the incident!
Result from the Day before accident: 07.09.2019
Wikipedia's reliable information on the location of the incident:

## Slide 23
What problems did we solve?
Our model can detect anomalous speed changes or directional changes of a vessel during a certain time period.
So if a accident is because of anomalous speed changes or directional changes,
After the accident, we can detect the accident by analyzing the AIS data.
But the model cannot predict accidents that do not occur.

## Slide 24
What is still lacking?
Due to the limitations of the data generation method, only anomalous changes in speed and direction can be identified
Solution: Find more realistic anomalous events or artificially set up more anomalous scenarios and simulate anomalous data based on them.
If the accident occurs between two segments, this accident is ignored by the model
Solution: Cut segments in different ways for the same trajectory so that different segment data can be generated for data enhancement.
For a more diverse set of anomalies, three features are not enough
Solution: Leverage features in AIS data and combine them with geographic information

## Slide 25: Q&A

## Slide 26
Contents
1. Motivation
2. Basic Information
3. Goal and Basic Ideas
4. Features Selection
5. Data Generation
6. Date Preprocessing
7. Model Selection
8. Train/Test Dataset
9. Evaluation
10. Results Analysis and Optimization of models and datasets
11. Real accident test
12. Ideas for improvement

## Slide 28: Model1
9. Optimization of models and datasets
1. use 2 features: SOG COG
Model2
1. use 3 features: Distance SOG COG
Dataset1 (Overfitting?)
Dataset2 (too little information?)
1. if there are less than 3 time point in one segment, drop it. otherwise supplement missing signals with 0
2. random missing data(at least 3 time point rest) in generation dataset, and supplement with 0
1. if there are less than 10 time point in one segment, Supplement missing signals with 0
2. no missing data in generation dataset
Dataset3 (the best)
1. if there are less than 5 time point in one segment, drop it. otherwise supplement missing signals with 0
2. random missing data(at least 5 time point rest) in generation dataset, and supplement with 0
Dataset4(just try)
1. All same as Dataset3 but the generation data seems like more unreal

## Slide 29
10.1 Statistics View of results
 | Dataset_1 | Dataset_2 | Dataset_3
Model_1 | Result_1 | Result_3 | Result_5
Model_2 | Result_2 | Result_4 | Result_6
Chart: Model Complare
| Result_1 | Result_2 | Result_3 | Result_4 | Result_5 | Result_6
Abnormal precision | 0.915 | 0.958 | 0.739 | 0.508 | 0.812 | 0.947
Abnormal recall | 0.827 | 0.885 | 0.298 | 0.579 | 0.616 | 0.804

## Slide 30
10. Comparing the performance of different models
10.1 Statistics View of results
 | Dataset_1 | Dataset_2 | Dataset_3 | Dataset_4
Model_1 | Result_1 | Result_3 | Result_5 | Result_7
Model_2 | Result_2 | Result_4 | Result_6 | Result_8
Chart: Model Complare
| Result_1 | Result_2 | Result_3 | Result_4 | Result_5 | Result_6 | Result_7 | Result_8
Abnormal precision | 0.915 | 0.958 | 0.739 | 0.508 | 0.812 | 0.947 | 0.848 | 0.962
Abnormal recall | 0.827 | 0.885 | 0.298 | 0.579 | 0.616 | 0.804 | 0.557 | 0.729

## Slide 31
10.2 Map View of results
Result 7
Result 8